## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 6 The Link Layer
and LANs

## Slide 2: Link layer, LANs: outline
6.1 introduction, services
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 3: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 4: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 5: Link layer services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, destination
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 6: Link layer services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 7: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 8: Adaptors communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 9: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 10: Multiple access links, protocols
two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 11: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 12: An ideal multiple access protocol
given: broadcast channel of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 13: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 14: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 15: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 16: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 17: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 18: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 19: Slotted ALOHA: efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
at best: channel
used for useful
transmissions 37%
of time!
!

## Slide 20: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 21: Pure ALOHA efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0-1,t0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
even worse than slotted Aloha!

## Slide 22: CSMA (carrier sense multiple access)
CSMA: listen before transmit:
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission
human analogy: don’t interrupt others!

## Slide 23: CSMA collisions
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 24: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
human analogy: the polite conversationalist

## Slide 25: CSMA/CD (collision detection)
spatial layout of nodes

## Slide 26: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 27: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 28: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 29: “Taking turns” MAC protocols
polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 30: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 31: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 32: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 33: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)

## Slide 34: LAN addresses and ARP
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 35: LAN addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 36: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 37: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 38: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 39: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 40: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 41: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 42: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 43: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 44: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 45: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 46: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star

## Slide 47: Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 48: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 49: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 50: 802.3 Ethernet standards: link & physical layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer

## Slide 51: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 52: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 53: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 54: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 55: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 56: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 57: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 58: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 59: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 60: Institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 61: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 62: VLANs: motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 63: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 64: Port-based VLAN
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 65: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1

## Slide 66: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
6.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 67: Data center networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center

## Slide 68
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)
Internet

## Slide 69
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 70: Link layer, LANs: outline
6.1 introduction, services
6.2 error detection, correction
6.3 multiple access protocols
64 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
6.5 link virtualization: MPLS
6.6 data center networking
6.7 a day in the life of a web request

## Slide 71: Synthesis: a day in the life of a web request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 72: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 73: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 74: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 75: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 76: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 77: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 78: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 79: Chapter 6: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS, VLANs
  virtualized networks as a link layer: MPLS
synthesis: a day in the life of a web request